## Slide 1: Nepal River Flood Prediction
Machine learning on daily weather and river-discharge data, 2023–2026
Notes: Overview: two ML tasks on the same Nepal river dataset — classify high-flow days and predict next-day discharge.

## Slide 2: Two questions, one dataset
13,390
daily records
10
river stations
2023–26
Jan 2023 to Aug 2026
12
weather and terrain inputs
Classification
Is the river in a high-flow state?
Target: discharge ≥ 90th percentile (27.84 m³/s)
Binary label, about 10% of rows are high-flow
Models: Logistic Regression, Decision Tree, Random Forest
Regression
How much water will flow tomorrow?
Target: next day’s discharge in m³/s, per station
Continuous value, range 0 to 3,176 m³/s
Models: Linear Regression, Random Forest, Decision Tree

## Slide 3: Ten stations across Nepal’s major basins
Station | River | Basin
Bahrabise | Bhote Koshi | Koshi
Belsot | Kamala | Kamala
Bhada Bridge | Babai | Babai
Chameliya/Nayalbadi | Chamelia | Mahakali
Chatara | Saptakoshi | Koshi
Chisapani | Karnali | Karnali
Devghat | Narayani | Narayani/Gandak
Khokana | Bagmati | Bagmati
Kusum | West Rapti | Rapti
Rasuwagadhi | Bhote Koshi | Narayani
Model inputs
Precipitation, rain, precipitation hours
Soil moisture (0–100 cm)
Temperature and dew point
Relative humidity
Wind speed, gusts, direction
Elevation and month
Current river discharge
Station, river, basin (one-hot)

## Slide 4: From raw data to evaluated models
1
Load and clean
Check duplicates and nulls (none found). Parse dates, drop unparseable rows.
2
Build targets
High-flow flag at the 90th percentile; next-day discharge via per-station shift.
3
Features
Numeric weather inputs plus month; one-hot encode station, river and basin.
4
Train models
Linear/logistic, Decision Tree, Random Forest. 80/20 split, seed 42.
5
Evaluate
Accuracy, precision, recall, F1; MSE, MAE, RMSE, R²; error and importance analysis.

## Slide 5: Classification: all three models score 99.9%
Confusion matrix, Logistic Regression (test set, n = 1,056)
Predicted normal
Predicted high
Actual normal
Actual high
961
True negative
1
False positive
0
False negative
94
True positive
99.9%
Accuracy
98.9%
Precision
100%
Recall
0.995
F1 score
Scores are identical across models and unusually high; see the caveats slide for why.

## Slide 6: Regression: Linear Regression leads on R²
Chart: R² on test set (higher is better)
| Linear Regression | Random Forest | Decision Tree
R² | 0.9196 | 0.8787 | 0.7314
Model | RMSE | MAE
Linear Regression | 22.45 | 6.69
Random Forest | 27.59 | 3.21
Decision Tree | 41.05 | 4.10
Typical vs. extreme days
Linear Regression has the lowest RMSE (22.45) and highest R² (0.92). Random Forest has the lowest MAE (3.21): closer on ordinary days, but larger misses on peaks.

## Slide 7: Today’s discharge drives tomorrow’s
Chart: Decision Tree feature importance, top 10
| River discharge | Soil moisture | Precipitation | Dew point | Month | Temperature | Precip. hours | Rain | Wind speed max | Humidity
Importance | 0.8313 | 0.0678 | 0.0642 | 0.008 | 0.0069 | 0.0068 | 0.0056 | 0.003 | 0.0022 | 0.0017
83%
of importance is current discharge: flow is highly persistent day to day
13%
comes from soil moisture and precipitation combined
<1%
each for temperature, wind, humidity and month

## Slide 8: Largest misses are monsoon peaks at Kusum
Top 5 errors, Linear Regression, all at Kusum (West Rapti), m³/s
Date | Actual | Predicted | Error
2024-09-12 | 661.2 | 213.0 | +448.2
2024-07-06 | 1,736.8 | 1,366.0 | +370.8
2025-07-12 | 482.1 | 218.0 | +264.1
2024-08-10 | 662.7 | 518.2 | +144.6
2026-08-03 | 335.5 | 234.4 | +101.2
All five dates fall in July–September. The model under-predicts sharp rises; dates are shown after correcting the day/month swap (see caveats).
+448
largest under-prediction (m³/s)
−76
largest over-prediction (m³/s)
9 of 10
largest errors are at Kusum

## Slide 9: Caveats to fix before trusting the numbers
1
Date parsing drops 61% of rows
dayfirst=True on ISO dates swaps day and month for days 1–12 and fails for 13–31. Only 5,280 of 13,390 rows are used and “month” is really day-of-month.
2
Target leakage in classification
The label is defined from river discharge, which is also an input. Near-perfect scores are expected.
3
Wrong predictions scored
Decision Tree and Random Forest metrics reuse the logistic model’s predictions, so all three rows match.
4
Split and threshold choices
Random split on time-series data; the 90th-percentile threshold is global, not per station.

## Slide 10: Next steps
Fix date parsing with pd.to_datetime(df['date']) and re-run both notebooks
Use a chronological split and per-station thresholds
Drop current discharge from the classifier, or predict tomorrow’s class
Add rolling rainfall and soil-moisture features; check monsoon extremes separately
Notes: Linear Regression is the current best for next-day discharge (R² 0.92). Classification scores need the leakage and date fixes before they mean much.